## Slide 1: NAIP Accuracy and Ground Control Point Collections
David Davis, USDA-FSA-APFO
FGCS Meeting
August 4, 2016

## Slide 2
Topics
Increasing the NAIP horizontal accuracy requirement
NAIP GCP Status Map
GCP collection by FSA personnel
Acronyms
APFO Aerial Photography Field Office
CLU Common Land Unit
FSA Farm Service Agency
GCP Ground Control Point
MDOQ Mosaicked Digital Ortho Quadrangle
NAIP National Agriculture Imagery Program

## Slide 3
NAIP Horizontal Accuracy
FSA uses photo-identifiable ground control points to inspect the horizontal accuracy of NAIP and other imagery programs. Prior to 2006 NAIP accuracy was determined with “relative control” by comparing new imagery to mosaicked USGS DOQQs (MDOQs).
For 10 years FSA has coordinated at the national, state, and local level as well as individual research to gather available GCPs for image inspection. A small number of GCPs were also purchased. Non-survey grade GCPs are also being acquired by FSA personnel. The data accuracy is suitable for checkpoints and not engineering or survey level work.

## Slide 4
Brief History of NAIP GCP Usage
2002 – 2008 full or partial use of relative control
2006 1 state, Utah (pilot project)
  GCPs provided to vendor for production
2007 1 state, Arizona (pilot project)
  GCPs provided to vendor for production
2008 Half & Half Half of states used GCPs and half used the relative control method
  GCPs IN, MN, NH, NC, TX, VT, VA
  Vendors not provided GCPs for production since no longer a pilot project
2009 to present – All states flown for NAIP have used absolute control for inspection

## Slide 5
NAIP Inspection & Requirements
The NAIP vendors and FSA both inspect the data to make sure it meets the task order requirements.
The inspection results have shown overall accuracy improvements year after year.
For the past four years the horizontal accuracy has been approximately 2-meters (requirement of 6-meters).
FSA inspection results:
  2008 – 2015: Average 2.8 meters (image to GCP difference)
  2015: 18,214 image locations reviewed with GCPs
  2015: Of 27 total states, only 3 above 2-m & 1 above 3-m

## Slide 6
NAIP Inspection & Requirements
After consulting with the NAIP funding partners and vendors, FSA changed the requirement to 4-m for 2016.
The specification is already being achieved, is not a new burden on the vendors, does not increase the product cost, and ensures a more accurate product for all.
NAIP Task Order:
“(b) Horizontal Accuracy. Unless otherwise specified in the individual task order, all well-defined points tested on DOQQ tiles shall fall within 4.0 meters of true ground at a 95% confidence level (see FGDC-STD-007.3-1998, page 3-10).”

## Slide 7
NAIP GCP Acquisition 2008 - 2011

## Slide 8
NAIP GCP Coverage
*Note areas of abundant and scarce coverage
2008 – 7,302
2009 – 31,055
2010 – 37,902
2011 – 38,618
2012 - ± 41,000

## Slide 9
FSA State Office GCP Collections
After coordinating with 100s of agencies and receiving 40000+ GCPs, some areas still lack coverage.
In 2012 various options, including GPS were investigated for obtaining GCPs, in the areas lacking coverage.
GPS equipment being used at that time in the FSA state and county offices was not suitable for GCP collections.
After extensive research FSA purchased a few GPS units & software for use by agency personnel to collect GCPs.
Currently three GPS units and software are being used.
  Geo XH & 7, TerraSync & Pathfinder Office

## Slide 10
FSA State Office GCP Collections
APFO and several FSA state offices developed and tested methods for GCP collections.
Standards, processes, forms, menus (data dictionaries), and best practices were developed.
Training materials & webinars provided by APFO to FSA state offices.
Schedules are established and equipment sent by APFO to FSA state offices for GCP collections.

## Slide 11
FSA State Office GCP Collections
Three states at a time have the devices for one month. Up to 12 states per year are able to collect GCPs for NAIP.
The equipment is sent back to APFO, the data processed, and the equipment is then sent to the next three states.
In some cases GCPs can be collected while personnel are in the field doing their regularly scheduled projects.
Training and processes are updated based on the successes or issues of the prior year or collection round.
Over 700 GCPs have been collected so far, with a total value of over $210,000. *Based on $300 cost per GCP if purchased

## Slide 12
FSA State Office GCP Collections
Along with training, preplanning is one of the keys to success
Determine areas of need, select potential GCP sites, & plan route
Willows
Hamilton City
Live Oak
Yuba City
GCPs: 12
Distance: 83 miles

## Slide 13
¿Questions
and
Comments?