## Slide 1: Spectrum Matters
FGCS/FGDC Meeting
4 August 2016
Larry Hothem
USGS, Reston, VA

## Slide 2: Topics
GPS adjacent band compatibility (ABC) assessment
  DOT
  NASCTN
Spectrum Repurposing & Interference with Space-Based PNT Services
GPS.GOV website – source for spectrum information
Communicating with IRAC/NTIA representatives on spectrum matters

## Slide 3: Adjacent-Band Compatibility (ABC)
A signal’s ability to operate free of harmful degradation (interference) from other transmissions in the nearby areas of the electromagnetic spectrum
Adjacent-band interference (ABI) can occur as the result of an adjacent band’s power and proximity to a signal as well as inadequate filtering and/or tuning
“L-BAND”
GPS L1
GPS L5
GPS L2
*National Telecommunications and Information Administration (NTIA) Table of Allocations in the L-Band (1-2GHz, IEEE)
Notes: L1: 1575.42 MHz L2: 1227.60 MHz L3: 1381.05 MHz L4: 1379.913 MHz L5: 1176.45 MHz
SGLS: 1783.74 MHz
SAR/GPS: Hosted Canadian Payload (Future), locate people for SAR (SV9+)
Info: Capital leaders is primary
Colors:
Light Orange: Radionavigation
Light Green: Radionavigation satellite
Maroon: Aeronautical Radionavigation

## Slide 4: GPS ABC Assessment Testing
Two DOT testing studies
  April 2016
  July 2016
Study objectives
  Evaluate allowable adjacent-band power levels, as a function of offset frequency, to ensure continued operation of all applications of GPS/GNSS services
    Consider future receiver development designed to use modernized GPS and interoperable GNSS signals
  Advance understanding of the extent to which such power levels impact devices used for a variety of GPS/GNSS applications
    A critical application is for transportation safety purposes

## Slide 5: GNSS Signals Used in Testing
Signal
GPS C/A-code
GPS L1 P(Y)-code
GPS L1C
GPS L1 M-code
GPS L2 P(Y)-code
SBAS L1
GLONASS L1 C or P
BeiDou B1I
Galileo E1 B/C

## Slide 6: April 2016 Testing Overview
Civil GPS Receiver Testing Conducted April 25-29, 2016, at the Army Research Laboratory's (ARL) Electromagnetic Vulnerability Assessment Facility (EMVAF), White Sands Missile Range (WSMR), NM
  DoD testing of military receivers was conducted the week before
Participants included:
  Federal agencies: NASA, NOAA, USCG, USGS, DOT, FAA
  Manufacturers: Trimble, Deere, Novatel, u-Blox, General Motors,
  Other: UNAVCO
  Independent Oversight Provided by MIT Lincoln Laboratory
80 receivers tested representing 6 categories of GPS/GNSS receiver usage: General Aviation (non certified), General Location/Navigation, High Precision & Networks, Timing, Space Based and Cellular
Underway is analysis of test data

## Slide 8: July 2016 Wired Testing
Federal Register Notice, July 7 2016, announces second round of ABC testing
Wired testing study objectives:
  Evaluate receiver characterizations for comparison with April 2016 chamber results
  Include Out-of-band (OOB) interference at prescribed and proposed levels w/Long Term Evolution (LTE) uplink & downlink signals
  Assess GNSS signal acquisition characterizations
  Make measurements for assessing antenna characterization
Test a limited number of the receivers previously tested in April:
  All six usage categories represented

## Slide 9: Wired Testing Overview
Tests executed 7/25-29 at Zeta Associates in Fairfax, VA
Same test instrumentation used for the radiated test
  GNSS playback (MITRE)
  (Zeta) Interference generation system with modifications to support Out-of-Band (OOB) and acquisition test requirements
Representative set of GNSS equipment from the previous radiated testing
  All six categories of usage were represented
  Approximately 14 receivers were tested
  Same receiver data collected as with radiated/chamber test
Antennas characterized separately in MITRE’s anechoic chamber
Independent oversight provided by MIT Lincoln Laboratory

## Slide 10: Receiver List
Agency | # of Rx | No. | Category | Receiver | Antenna | Test Loc. | Active Ant.
Zeta | 1 | Mezz | TIM | NovAtel |  |  | Yes
FAA | 20 | 24 | GAV | Garmin - GPSMap 696 | AeroAntenna Technology Inc AT2775-41-TNCF | H7 | No
 |  | 40 | TIM | Trimble SMT360 GPS receiver | Trimble SMT-360 Antenna | I6 | Yes
USDOT | 16 | 51 | HPR | NAVCOM SF3050 |  | B6 | Yes
 |  | 56 | CEL | Android S5 |  | A6 | No
UBLOX | 5 | 61 | GLN | EVK-M8N |  | I9 | No
NOAA | 9 | 11 | HPR | Javad Delta II | JAVAD JAVRINGANT_DM | I3 | Yes
 |  | 12 | HPR | Septentrio PolaRx4Pro | AERO AERAT1675_120 | I4 | Yes
 |  | 13, 14 | HPR | Trimble NETR5 | Trimble TRM55971.00, Trimble Zephyr 59800-00 | G4, K5 | Yes
 |  | 15 | HPR | Trimble NETR9 | Trimble TRM29659.00 | K4 | Yes
 |  | 16, 18 | HPR | Leica GRX1200GGPRO | Leica AX1202GG, LEIAT504 | E4, E3 | Yes
 |  | 17 | HPR | Trimble 5700 | Trimble TRM41249.00 | G3 | Yes
 |  | 19 | HPR | Trimble NETRS | Ant com Active L1/L2 | E5 | Yes
UNAVCO | 5 | 77 | HPR | Septentrio PolaRx5 (Enabled) |  | I13 | Yes
 |  | 78 | HPR | Septentrio PolaRx5 (Disabled) | Choke Ring | K13 | Yes
NASA | 8 | 3 | SPB | TriG | Choke Ring | C2 | Yes

## Slide 11: National Advanced Spectrum and Communication Test Network (NASCTN)
Project: Impact of LTE Signals on GPS Receivers
  Proposed by Ligado Networks
Draft test plan distributed May 2016
Briefing for PNT agencies held June 13
  DOT sent comments and concerns to NASCTN Project Manager, July 6, 2016
  Key concern: limitations of test data given proposed scope of study plan
Revised test plan distributed July 22, 2016
Other Concerns:
  Test wasn’t announced in Federal Register
  Ligado defined the scope of the project
Public details found in article published July 27, Inside GNSS News
http://www.nist.gov/ctl/nasctn/impact-of-lte-on-gps-receivers.cfm

## Slide 12: Spectrum Repurposing & Interference with Space-Based PNT Services
Reference June 13 letter – PNT Advisory Board to PNT EXCOM
Concern with repurposing frequency bands adjacent to GPS to allow high-power terrestrial broadband services
GPS is a space-based navigation system – one-way signals; not a terrestrial-based two-way signal communication system
  A fundamentally different use of the spectrum
  Conflicts with principal allocation of band adjacent to GPS L1 signal – the Mobile Satellite Services (MSS)
Proposed “sharing” of spectrum in bands adjacent to GPS and other GNSS is only possible among compatible systems
Recommends key criteria for assessing interference to GPS & GNSS signals
  Any new spectrum proposals must not affect existing & evolving uses of space-based PNT services
  Protect all classes of GPS/GNSS receivers
  Protect all receiver operating modes, including signal acquisition/reacquisition
  Protect all uses of all emerging GNSS signals

## Slide 13
Spectrum information available at the website for the PNT National Coordination Office (NCO)

## Slide 14
http://www.gps.gov/spectrum/ABC/
Spectrum information available at the website for the PNT National Coordination Office (NCO)

## Slide 15
CHECKS & BALANCES SPECTRUM MANAGEMENT SYSTEM
COMMUNICATIONS ACT OF 1934
COORDINATION
ADVISORY
LIAISON
INTERDEPARTMENT RADIO ADVISORY COMMITTEE (IRAC)
NTIA Chairs IRAC & Subcommittees
20 Govt Departments/Agencies as Members
NTIA
- National Defense
- Law Enforcement &
Security
- Transportation
- Resource Mgt Control
- Emergencies
- Other Services
(On behalf of President)
FCC
(Independent Agency)
- Business
- State & Local
- Entertainment
- Commercial
- Private
Communicating with IRAC/NTIA representatives on spectrum matters

## Slide 16: Thank you