## Slide 1
OPUS Projects to the IDB
Mark Schenewerk
816-994-3067
mark.schenewerk@noaa.gov

## Slide 2
OPUS-Projects offers web-based tools to process GPS surveys.
What is OPUS-Projects?
  Data uploads through OPUS.
  Multi-station, multi-session processing with PAGES.
  Management and control through a GUI.
Notes: Since going operational in 2014, 2400 people have received training; 9000 projects are currently in existence.

## Slide 3
This project, “Deriving a valid path for OPUS-Projects GPS projects to be loaded to the NGS IDB,” will make OPUS-Projects correctly and completely submit GPS survey results for publication to the IDB. That title is a mouthful so call it simply “OP to IDB.”
Tasks include:
  Address any OPUS-Projects shortcomings.
  Build “one click” submission to the IDB.
  Demonstrate this in a beta version of OPUS-Projects: available for public comment in early 2017.
What is “OP to IDB?”

## Slide 4
“OP to IDB” falls under Goal 2, Objective 3 of the NGS Strategic Plan: “Reinvent Bluebooking.”
But I say this project’s goal isn’t to reinvent bluebooking per se, but to reinvent how folks bluebook.
We hope to make data processing and bluebooking so simple and fool-proof that folks will submit surveys for publication to the IDB without trepidation.
Our nefarious plan ...
Notes: We also think this will make NGS quality control and validation of submissions simpler and faster.

## Slide 5
Automatically organize the data.
Simplify the processing.
Offer defaults tailored to the survey’s specs.
Automate file creation.
Quality control from start to finish.
A “green board” and you’re good to go.
How do we do this? K.I.S.S.

## Slide 6
Let OPUS-Projects perform all of the dull, error-prone, detail work.
That lets surveyors be surveyors …
  Collect quality data.
  Document field procedures, hardware and marks.
… and NGS be NGS.
  Formatting, quality control and validation.
  Datum densification and maintenance.
Let the tech work for us!

## Slide 7
The first “OP to IDB” task is OP vs IDB: a comparison of OPUS-Projects results to the corresponding published coordinates.
  This will result in action items and design requirements for the next generation OPUS-Projects.
  This will also serve as a basis for evaluating the next generation OPUS-Projects.
  In other words, OP vs IDB is the foundation for and justification of all subsequent work.
OP vs IDB

## Slide 8
11 Atlantic.
3 Great Lakes.
2 Midwest.
5 Great Plains.
2 mountain West.
0 Southwest.
3 Gulf coast.
1 in Alaska.
3 in the Pacific.
© Google INEGI. © Copyright 2016 Ursus Software, LLC.
What surveys were selected?
Notes: We have 37 projects in hand at this moment:
28 primary projects
5 FAA airport surveys.
Several HtMod-like surveys.
Urban/rural, coastal/inland, … surveys.
2 surveys with occupations 1 - 2 hrs in duration.
5 “mimics” (CORS data windowed 2 hrs).
2 held for testing beta with more to come(?).

## Slide 9
Most surveys were completed in 2011 - 2013.
All seasons are sampled.
Number of passive marks in a survey ranged from 1 to 40.
Total survey durations ranged from 1 - 340 days.
What are these survey like?
Notes: Median number of marks in a survey was 7.
Median number of days in a survey was 4.

## Slide 10
Every survey was processed by two team members.
No effort was made to duplicate the original processing. Rather, all processing followed recommended OPUS-Projects guidelines (Mader, 2014).
Spreadsheets of the OPUS-Projects - published NAD 83 (2011) epoch 2010 coordinate differences were created.
Next: process the surveys in OPUS-Projects.
Notes: One nearby hub common to all session processing.
One distant CORS (≳ 1000 km).
7200 s, piecewise linear tropo correction.
15° elevation cutoff.
NORMAL constraint weight.
Problematic marks were excluded at the team member’s discretion.

## Slide 11
For the 324 passive marks in 28 surveys, the mean coordinate differences are:
ΔN: -0.1±0.7 cm ΔE: 0.1±1.0 cm ΔU: -0.2±2.3 cm
OP - IDB results.
For the 324 passive marks in 28 surveys, the mean coordinate differences are:
ΔN: -0.1±0.7 cm ΔE: 0.1±1.0 cm ΔU: -0.2±2.3 cm
Notes: Uncertainties are all 1 sigma population standard deviations.

## Slide 12
OP - IDB conclusions.
Making no effort to duplicate the original processing, we found:
  The mean coordinate differences are zero.
  The results are slightly skewed, but reasonably close to normal distributions.
  These results meet the de facto ±2 cm horizontal and ±4 cm vertical CORS accuracies.
  These results exceed the NGS-58 (Zilkoski et al., 1997) 5 cm vertical accuracy target.

## Slide 13
At least 5 surveys have description (b-file) errors.
At least 2 surveys used out-of-date CORS information.
Questionable quality control decisions were made in both the original and OPUS-Projects processing.
OPUS-Projects struggled with integer fixing on very long baselines and with short occupations.
OPUS-Projects struggled with surveys in remote locations.
At least 6 surveys displayed biases relative to their published coordinates.
Issues to address.

## Slide 14
Applying the passive + CORS constraints in OPUS-Projects or the CORS-only constraints to the original g-files reduced the biases.
A quick aside about the OP - IDB biases.

## Slide 15
Technical issues
  ADJUST for GPSCOM.
  Update integer fixing.
  Offer alternate session definitions.
  Improve quality control.
Bluebooking.
  “Finish” the b- and g-files.
  Edit/upload a serfil.
  Upload(/create?)/edit a description file.
  Create a submission “package”.
Update documentation and training materials.
Changes planned for the OPUS-Projects.

## Slide 16
Now: Finish the OP vs IDB report.
Sep: Complete OPUS-Projects dev.
Oct: OPUS-Projects dev release for NGS comment.
Oct: PSC OK to go to beta.
Nov: Catch our breath: work on documentation.
Jan: OPUS-Projects beta released for public comment.
What next?
OP 2 IDB Evaluation/Comparison
Load/Process Projects
Jun
Jul
Oct
Nov
Dec
Jan
Feb
Mar
Apr
May
Aug
Sep
Oct
Nov
NGS Presentation
PSC
FGCS Presentation
Comment
Public webinar
E/C Reort
Load/Process Projects
OP 2 IDB Evaluation/Comparison
Comment
Beta OP
Public Presentation
Close out
Dev OP
Sep
Dec
E/C Report
Jan
Feb
Mar
PSC
FY16
FY17
PSC
FGCS Presentation
Development Plan

## Slide 17
OPUS Projects to the IDB
Mark Schenewerk
816-994-3067
mark.schenewerk@noaa.gov